# How to use the SkoleSYS buildtools
## skolesys-deb
skolesys-deb[-r svn_repos][-l iso_dir][-t tgz_dir][--dont-fetch] module_name
This tool is used to create deb-files for distribution. It can fetch distribution content using svn, iso or tgz. Each deb-file is controlled by a debinfo file, the naming convention for such a file is <module_name>_debinfo.py - e.g. the module named "python-skolesys-client_feisty" should be named: "python-skolesys-client_feisty_debinfo.py". Module name should not be confused with package name, the package name is specified inside the debinfo file.
Describing the naming convention has already revealed that the python interpreter is used for parsing debinfo files, and that is also why I say module name instead of package name. A debinfo file consists of a number of global variables, most of these are optional but there are three mandatory:

Name	Type	Description
fetch_method	string	Specify how to fetch the content for the deb-package.
control	dict	This dictionary holds the normal dpkg control structure.
copy	dict	Specify which files should go where in the filesystem during installation.

Tabel 1:Madatory debinfo variables

Name	Type	Description
svn_module	string	When using subversion as fetch method you can use this variable to specify a certain path in the repository repository. If this variable is not set skolesys-deb will try to use the module_name for fetching.
svn_repos	string	Specify the subversion repository to fetch the package source from. If this variable is set it will override the SKOLESYS_SVNBASE environment variable but not the command line argument -r.
links	dict	Each key-value entry in the links dict specifies a symbolic link to be created in the filesystem after installation.
perm	dict	The perm variable can be used to setup filepermissions in for the files being installed.
preinst	string	Pre-installation script.
postinst	string	Post-installation script.
prerm	string	Script to be executed before uninstallation.
postrm	string	Script to be executed after uninstallation.

Tabel 2:Optional debinfo variables
### Subversion based modules
Most of the skolesys-deb modules rely on fetching their content from a subversion repository. It is possible to setup this repository once and for all by setting the SKOLESYS_SVNBASE environment variable. However, if you need to fetch content for different skolesys-deb modules from different repositories you can specify the repository for each module by setting the svn_repos variable in the debinfo file or you can do it by using the -r command line option. svn_repos will override SKOLESYS_SVNBASE, -r command line options overrides everything.
The debinfo variable svn_module specifies the path to fetch from inside the repository. If svn_module is unset skolesys-deb will try to fetch using the module_name as path.
Note: If you need to fetch from the base of a repository you will have to set svn_repos to the repository's parent dir – so if I need to fetch from the root of the repository located at svn.mydomain.org/srv/svn/skolesys I will need to set svn_repos to somthing like svn+ssh://svn.mydomain.org/srv/svn/ and svn_module to skolesys.
### ISO and tar.gz based modules
There is not much to say about these skolesys-deb module types. All skolesys-deb needs to know is basically where to find the iso or tgz files. Like in subversion based skolesys-deb modules you can set environment variables that will serve as default directories for iso/tgz file hunting. command line options -l iso_dir and -t tgz_dir can also be used to set the directory location and these will of course override the environment variables if set.
SKOLESYS_ISODIR	The default directory when searching for ISO files.
SKOLESYS_TGZDIR	The default directory when searching for tgz files.